## Slide 1
THE BLACK SEA NOWCASTING/
FORECASTING SYSTEM

## Slide 2
http://www.aos.princeton.edu/WWWPUBLIC/htdocs.pom/
THE PRINCETON OCEAN MODEL
(A sigma coordinate, free surface, ocean model, which includes
a turbulence sub-model)

## Slide 3
THE MAIN FEATURES OF THE POM
-contains an embedded second moment turbulence closure sub-model
to provide vertical mixing coefficients;
-it is a sigma coordinate model in that the vertical coordinate is scaled on
the water column depth;
-it uses an explicit scheme (for horizontal advection and diffusion) and implicit (for
vertical diffusion) as well ;
-the model has a free surface and a split time step
Transformation from rectangular ( x, y, z )
to sigma ( x', y', s ) coordinates:
x = x', y= y', s =(z-h)/(H+h)

## Slide 4
THE BLACK SEA CIRCULATION MODEL
The maximum depth is equal to 2150 m. The area is covered with the grid
which has space step of 4.8 km (236 x 130 meshes). The model has 36
non-uniformly spaced levels in s -coordinates. Time step for the internal mode
is equal to 10 min, and for external – 6 s, so 1 day consists of 144 time steps
of internal mode.

## Slide 5
METEOROLOGICAL FIELDS USED FOR FORECAST
(boundary conditions on the surface)

## Slide 6
SATELLITE ALTIMETER DATA
Tracks of T/P and Jason (black points), ERS1,2 EnviSAT (red points)
and GFO (blue points) for the Black Sea area

## Slide 7
SEA SURFACE TEMPERATURE
(Images of Very High Resolution Radiometer (AVHRR), NOAA satellites.
The data are received and processed in Marine Hydrophysical Institute.
The final product has space resolution of about one kilometre.)

## Slide 8
STEERING PARAMETERS
The most essential changeable parameters are contained in the file “param.txt”.
“time” – sets the initial time moment (time=0.0 corresponds to 1Jan1992 00hr);
“nread” - restart parameter: if nread=0 then run begins from initial fields,
if nread=1 then from intermediate fields, which are written in the file “restart”;
“idays” - number of days to run;
“irest” - interval (in time steps) of writing “restart” file;
“ioutint” - interval (in time steps) of writing “out.dat” file and displaying on the screen
some integral parameters.
“ioutf” - the frequency or writing output fields in the folder “12”;
“nsst” - assimilation of SST flag, if nsst=1 then you run the model with assimilation of SST,
if nsst=0 then without;
“nas” - assimilation of altimetry flag, if nas=1 then you run the model with assimilation ,
if nas=0 then without;
“nest” - flag for writing data for the nesting model, if nest=1 then file is written, if nest=0 then not.
“lnest” - the frequency or writing fields for the nested model.

## Slide 9
INSTALLATION THE BLACK SEA
BASIN-SCALE MODEL
ftp://mhi.net.ua
User name: ratner
Password: “nj>hfHfnyth

## Slide 10
VISUALIZATION OF OUTPUT DATA
Grid Analysis and Display System (GrADS)
(http://www.iges.org/grads/ )
The Grid Analysis and Display System (GrADS) is an interactive desktop tool that
is used for easy access, manipulation, and visualization of earth science data.
The format of the data may be either binary, GRIB, NetCDF, or HDF-SDS
(Scientific Data Sets).
GrADS uses a 4-Dimensional data environment: longitude, latitude, vertical level,
and time. Data sets are placed within the 4-D space by use of a data descriptor file.
Data may be displayed using a variety of graphical techniques: line and bar graphs,
scatter plots, smoothed contours, shaded contours, streamlines, wind vectors, grid
boxes, shaded grid boxes, and station model plots. Graphics may be output in
PostScript or image formats.
GrADS has a programmable interface (scripting language) that allows for sophisticated
analysis and display applications.